## Slide 1: Smart Grid – Controlling the Edge
Dr. Sonja Glavaski, Program Director

## Slide 2: Mission & History of ARPA-E
2007
Rising Above
the Gathering Storm
Published
America COMPETES
Act Signed
2009
American Recovery & Reinvestment Act Signed
2011
2012
2013
2014
2010
1
37
7
12
16
20
23
Programs
To Date
Awards Announced
2015
32
America COMPETES
Reauthorization Signed
$275 Million
(FY2012)
$280 Million
(FY2015)
500+
2016
39
$280M
(FY14)
2017
Coming
soon
$400M
(Recovery Act)
$180M
(FY11)
$251M
(FY13)
$291M
(FY16)
$280M
(FY15)
$275M
(FY12)
$280M
(FY14)
Mission: To overcome long-term and high-risk technological barriers in the development of energy technologies
Notes: Updated to reflect 2015 numbers
Budget (Million) Data Source:
FY2009: $15,000 http://energy.gov/sites/prod/files/FY11Orgsum.pdf ARRA $388,856 http://energy.gov/sites/prod/files/FY11Orgsum.pdf (Note: rounded to $400 million in all public documents, did so here to maintain consistency.)
FY2010 $0 http://energy.gov/sites/prod/files/FY11Orgsum.pdf
FY2011 $179,640 http://energy.gov/sites/prod/files/FY13Volume4.pdf (p. 401)
FY2012 $275,000 http://energy.gov/sites/prod/files/2013/04/f0/orgsum.pdf
FY2013 $250,636 http://energy.gov/sites/prod/files/2014/04/f14/FY%202015%20DOE%20Budget%20by%20Organization.pdf
FY2014 $280,000 http://energy.gov/sites/prod/files/2015/01/f19/FY2016BudgetSummaryTableByOrg_0.pdf
F2015 $279,982 http://energy.gov/sites/prod/files/2015/01/f19/FY2016BudgetSummaryTableByOrg_0.pdf
FY2016 (Requested) 325,000 http://energy.gov/sites/prod/files/2015/01/f19/FY2016BudgetSummaryTableByOrg_0.pdf

## Slide 3: Focused Program Portfolio
charges
Nodes
geni
Grids
Heats
IONICS
GRID DATA
Electricity
Generation
alpha
focus
Rebels
GENSETS
Mosaic
Impacct
Solar Adept
Range
amped
beest
ElectroFuels
Move
Remote
Petro
TERRA
Transnet
NEXTCAR
REFUEL
Efficiency &
EMISSIONS
arid
delta
Metals
Monitor
Switches
SHIELD
Adept
beetit
React
ROOTS
ENLITENED
Grid &
Grid storage
Transportation &
Storage
OPEN 2009, 2012, & 2015 Solicitations
Complement Focused Programs
Active
Alumni

## Slide 4: U.S. Power Grid

## Slide 5
US Grid Today in Few Words
DISPATCHABLE
RENEWABLE
GENERATION
DISPATCHABLE
GENERATION
NON-DISPATCHABLE
RENEWABLE
GENERATION
STORAGE
DISTRIBUTED ENERGY RESOURCES (DERS)
Top down management
Control generation to match load
Distribution treated as net-load
Planning for highest peak load
Notes: The Grid: Bulk generation, transmission, distribution,
The dominant paradigm for delivering electricity in the U.S. consists primarily of bulk electricity generation at central power plants, followed by transport across the U.S. electrical grid via transmission and distribution (T&D) networks, and finally delivery to the end-user.
Bulk Generation
dispatchable thermal generation (nuke, coal, NGCC),
dispatchable renewables (hydro), and
non-dispatchable renewables (solar, wind)
The addition of intermittent generation along with changing usage patterns (e.g. increased penetration of electric vehicles) is leading to greater uncertainty and variability in the electric grid.

## Slide 6: Grid Reliability - Frequency Stability
Directly affected by generation-demand balance
60 Hz
Primary Frequency Ctrl
Automated Generation Control (AGC)
Slope ∝ System inertia
0 s
5-10 s
20-30 s
5-10 min
System Frequency
Time
Contingency Event
UFLS Threshold
Frequency Nadir
Settling Frequency
~59.5 Hz

## Slide 7: Who Manages U.S. Grid Reliability?
3 primary electric grids in US
8 regional entities managing electricity reliability

## Slide 8: Who Oversees U.S. Whole Sale Markets?
RTO/ISOs
Operate the transmission grid
Dispatch electricity based on marginal cost bids

## Slide 9: U.S. Power Grid is Changing!
WA: 15% x 2020*
OR: 25%x 2025*
(large utilities)
CA: 50%
x 2030
MT: 15% x 2015
NV: 25% x
2025*
UT: 20% x 2025*†
AZ: 15% x 2025*
ND: 10% x 2015
NM: 20%x 2020 (IOUs)
HI: 100% x 2045
CO: 30% by 2020 (IOUs) *†
OK: 15% x 2015
MN:26.5%
x 2025 (IOUs)
31.5% x 2020 (Xcel)
MI: 10% x 2015*†
WI: 10% 2015
MO:15% x 2021
IA: 105 MW
IN: 10% x 2025†
IL: 25% x 2026
OH: 12.5% x 2026
NC: 12.5% x 2021 (IOUs)
VA: 15% x 2025†
KS: 20% x 2020
TX: 5,880 MW x 2015*
SD: 10% x 2015
SC: 2% 2021
NY: 29% x 2015
Renewable portfolio standard
Renewable portfolio goal
29 States + Washington DC have a Renewable Portfolio Standard (8 states have renewable portfolio goals)
CAISO opening markets to DERs (50% by 2030)
NY Reforming the Energy Vision to increase renewables & DERs (50% by 2030)
Hawaii to use only renewable power within the next 30 years (100% by 2045)
Vermont to use mainly energy from green sources (90% by 2050)

## Slide 10: Grid Change Brings Challenges
Dispatched generation
Predictable load
Capacity available
Intermittent DG
Variable
Net-Load
Capacity constrained
Renewables penetration is limited (< 30%) because of lack of capability to reliably and affordably manage its variability

## Slide 11: Emerging Grid Operation Paradigms
ISO & DER aggregators
  ISO manages transmission & wholesale
  Aggregated DERs bid into bulk market
ISO & DSO
  ISO manages transmission & wholesale
  DSO manages distribution & retail
Network of micro-grids
  Power supplied locally
  Grid supplies backup power

## Slide 12: Network Optimized Distributed Energy Resources (NODES) Program

## Slide 13
If we can actively control Net-Load,
50% renewable integration is possible.

## Slide 14: NODES Network Optimized Distributed Energy Systems
Goals
Enable renewables penetration at > 50%
Improve overall grid efficiency & reliability
Reduce CO2 emissions
Guarantee Level-of-Service to the Grid
Guarantee customers’ QoS
Mission
Reliably manage dynamic changes in the grid by leveraging flexible load and Distributed Energy Resources’ (DERs) capability to provide ancillary services to the electric grid at different time scales.
Project Categories | Response Time | Ramp Time | Duration
C1: Synthetic Frequency Reserves | < 2 sec | < 8 sec | > 30 sec
C2: Synthetic Regulating Reserves | < 5 sec | < 5 min | > 30 min
C3: Synthetic Ramping Reserves | < 10 min | < 30 min | > 3 hr

## Slide 15: Category 1: Synthetic Frequency Reserves
Objective
Increase “inertia” in the system
Approach
Load providing inertial response while
using local measurements
Challenges
Guarantee stability of the system
Guarantee improvements of
frequency compared to the
traditional generation control only
Response speed
Validation
HIL validation with a minimum of 100 actual devices at power
Large-scale simulation (optional) to demonstrate the robustness and scalability
Inertial Response
Droop Control

## Slide 16: Category 2: Synthetic Regulating Reserves
Objective
Support frequency recovery/stability of the system
Approach
Use coordinated net-load control to
adjust magnitude and shift in time
Challenges
Coordination of large number of
heterogeneous energy resources
Understanding trade-off between
peer-to-peer communication and
optimal performance
Validation
HIL validation with a min of 100 actual devices at power
Large-scale simulation (optional) to demonstrate the robustness and scalability
If successful, load adjustment + shift could help
enable 50% renewables at 92% utilization
Droop Control

## Slide 17: Category 3: Synthetic Ramping Reserves
Objective
Coordinated long term shifting of load with thermal/electric
storage (buildings, warehouses), and non-critical load
(pool pumps, PEVs) to reduce curtailment of renewables
Approach
Forecasting aggregated loads capacity
Supervisory control enabling load
balancing signal tracking
Challenges
Modeling and control of
a populations of controlled loads
Determining control requirements for
guaranteed aggregate load performance
Validation
Large-scale simulation to demonstrate the robustness and scalability
If successful, load adjustment + shift (>10%) could enable 50% renewables at 95% utilization
Droop Control

## Slide 18: NODES Project Portfolio
Category 1: Synthetic Frequency Reserves
Category 2: Synthetic Regulating Reserves
Category 3: Synthetic Ramping Reserves

## Slide 19: NODES Projects by Team Lead Geography
$33.85M/$42.53M Program to accelerate technologies that Improve the Efficiency and Reliability of the U.S. Electrical Grid
PNNL
$2.66M
PNNL
$2.66
PNNL
$2.66M
UMN
$2.95M
PNNL
$2.66M
Northwestern U.
$2.69M
PNNL
$2.66M
Eaton Corp.
$3.02M
PNNL
$2.66M
U. Vermont
$1.69M
PNNL
$2.66M
DNV GL
$2.15M
PNNL
$2.66M
General Electric
$4.05M
PNNL
$2.66M
NRECA
$1.33M
PNNL
$2.66M
NREL
$3.90M
PNNL
$2.66M
ASU
$3.00M
PNNL
$2.66M
UCSD
$2.57M
PNNL
$2.66M
Stanford U.
$3.83M
Category 1
Category 2
Category 3
Notes: Dark Blue = Category 1
Light Blue = Category 2
Orange = Category 3
PNNL: 1, 2, 3
UMN: 1, 2
NU: 1
Eaton: 2
UVM: 2
DNV-GL: 2
GE: 2,3
NRECA: 1,3
NREL: 1,2
ASU: 3
UCSD: 2
Stanford: 2,3

## Slide 20: NODES Projects by Team Members Geography
M
PNNL
M
UMN
NU
UVM
NRECA
NREL
6M
UCSD
Stanford
Category 1
Category 2
Category 3
SNL
ASU
Nexant
PJM
DNV-GL
Group NIRE
GE
M
Eaton
CMU
SparkMeter
SCE
GELI
6M
Caltech
M
Harvard
ANL
OPAL-rt
CPS Energy
M
Spirae
6M
Typhoon
6M
UIUC
6M
Dynapower
M
UTK
UMICH
MIT LL
Cornell
LLNL
LBNL
SLAC
Google
Tesla
UF
Notes: Dark Blue = Category 1
Light Blue = Category 2
Orange = Category 3
PNNL: 1, 2, 3
UMN: 1, 2
NU: 1
Eaton: 2
UVM: 2
DNV-GL: 2
GE: 2,3
NRECA: 1,3
NREL: 1,2
ASU: 3
UCSD: 2
Stanford: 2,3

## Slide 21: Next Steps
Recruit Industrial Advisory Board (IAB) Members for teams
01
Develop grid management & control technology enabling large scale flexible loads & DERs integration
02
Validate solutions in HIL & Large Scale Simulation
03
Work with teams & IABs on technology to market plans and strategies
04
Engage Industry
Address Technology Needs
Demonstrate Novel Capabilities
Commercialize Technology

## Slide 22: Members of Industrial Advisory Boards

## Slide 23: NODES Projects Test Sites Geography
Ames, IA
Philadelphia, PA
Fort Collins, CO
Greenwood, DE
Champaign, IL
East Hartford, CT
San Diego, CA
San Ramon, CA
Rutland, VT
Lubbock, TX
South Burlington, VT
Minneapolis, MN
Golden, CO
Ramsey, MN
Cleburne, TX
Category 1
Category 2
Category 3
Westminster, CA

## Slide 24: Nationwide Cheap Power Super Highway
U.S. Power Grid of the Future
Ubiquitous Sensing and Data Collection
Seamless Integration of DERs
Active Customer Engagement
Strengthened Resiliency and Security

## Slide 25
www.arpa-e.energy.gov
Dr. Sonja Glavaski
Program Director
Advanced Research Projects Agency – Energy (ARPA-E)
U.S. Department of Energy
sonja.glavaski@hq.doe.gov
202-287-6146